## Slide 1
CE
Ref
W1
W2
Use a « Dummy » electrochemical cell made of an assembly of resistors and connect as shown here:
Wiring
~ 1KOhm
~ 500 KOhm
~ 5KOhm

## Slide 2
Reading of E1/E2/ET1-Ref/ET2-Ref/I1/I2
Coarse and fine adjustment of an offset applied to W1 : set to 0 if switch on downward position
Switch to disconnect internally the CE: keep the upward position
Switch to set a high input impedance on the ref (to minimize noise on low current measurement): : keep the upward position
The input voltage applied to W1 (substrate) will be multiplied by either 1, 0.1 or 0.01: set to 1
Output multiplying gain for the current (voltage) measured at W1 (substrate)
The input voltage applied to W2 (probe) will be multiplied by either 1, 0.1 or 0.01: set to 1
Coarse and fine adjustment of an offset applied to W2 : set to 0 if switch on downward position
Output multiplying gain for the current (voltage) measured at W2 (probe)
Bipotentiostat description
ET1 and ET2 stand for « Working electrode » W1( substrate) and W2 (probe)